## Slide 1: Experiments in Quantum Communication
Ayan Biswas, Anindya Banerjee, Rupesh Kumar,
Pooja Chandravanshi, M.V. Jabir, Nijil Lal, Ali Anwar, Sarika Mishra, Anju Rani, Tanya Sharma, Vardaan Mongia, Sandeep Singh, Jayanth, G.K. Samanta, Shashi Prabhakar, R. P.
Quantum Science & Technology Program
Atomic, Molecular and Optical Physics Division
Physical Research Laboratory (PRL), Ahmedabad

## Slide 2: Physical Implementation
Heralded Single Photons
Coherent Weak Laser Pulses
Optical Fiber
Free Space
Avalanche Photodiode SPD
Superconducting Nanowire SPD
Source
Transmission Channel
Detectors
Entangled photons
Homodyne detectors

## Slide 3
Classification of QKD

## Slide 4: Progress
Weak Coherent Pulse
Implementation of BB84 QKD protocol in free space for 200 meters with weak coherent laser pulses, and heralded single photon source
Rigorous characterisation of mean photon number per pulse – JLWT 2024
Side channel for BB84, source and detection, using a new technique based on cross-correlation - IEEE J. Quantum Electron (2021, 2023)
New QKD protocol – CD Protocol – gives higher key rate compared to BB84/Decoy state protocol for same mean photon number per pulse – Optics Continuum (2022)
Entrapped Pulse CD Protocol - Adv. Quantum Technol. 2025, 2400685
Entangled Photons
Development of bright entangled photon source at 810 nm (105 photon pairs per second) - Scientific Reports (2017), Advances in Quantum Technologies (2023)
~100 m
~100 m
Transmitter
Receiver
Reflector
Left: Field implementation
of free space QKD
Right: Compact entangled
photon source (810 nm)
developed at PRL

## Slide 5: Progress….
Implementation of BBM92 QKD protocol in free space for 200 meters with entangled photons, Sift Key rate (~4.5 kbps) and Secure Key rate (~2 kbps), QBER < 5% and effect of aerosols on the key rate - Journal of Optics (2022)
End to end encryption for audio and video with Space Application Centre (ISRO), Ahmedabad for free-space channel of 300 meters using BB84 as well as BBM92 protocol (ISRO Press Release)
Integration of fibre-based QKD with free-space QKD – free-space to fibre and fibre to free-space (C-DOT Press Release)
10. Device Independent QKD protocol using entangled photons (arXiv:2307.02149)
11. Working on entanglement swapping in free-space atmospheric channel of ~200 m
CV QKD
12. Experimental Shot Noise Measurement Using the Imperfect Detection (IEEE J. of Quantum Electronics 2023)
13. Free space continuous variable Quantum Key Distribution with discrete phases, ~5 m in lab (Physics Open 2023)
14. Gaussian Modulated CV QKD through free space, ~5 m in lab (Post-processing of data – Information reconciliation)
15. Working on field implementation (~200 m atmospheric channel) of discrete phase and Gaussian modulation CV QKD
16. Effect of turbulence on key rate – ongoing
17. Experimental simulation of satellite downlink and uplink

## Slide 6
A General Schematic for P&M QKD

## Slide 7
Experimental arrangement for CD-EPCD Protocol same as BB84-Decoy

## Slide 8
Key rates
Lim et al., Opt. Express 2017, 25, 11894
Assumption: No PNS, No USD

## Slide 9
Experimental Parameters

## Slide 10
Experimental and theoretical results
We use SDP technique to find
The bounds on the yields and
errors to compute the bounds
on key rates

## Slide 11
Key rates and Optimisation

## Slide 12
Entanglement distribution
over 200 meters

## Slide 13
Correlation of polarization states between Alice and Bob
Coincidence window = 1 ns
H | V | D | A
94.2% | 93.66% | 83.33% | 87.53%
Bell’s Parameter
S=2.54 ± 0.06
Polarization Visibility
Entanglement Distribution over 200 meters

## Slide 14
Parameter Estimation for BBM92 Protocol
Channel Transmissivity =0.70 Overall Detector Efficiency=0.4
 | H | V | D | A
H | 1023 | 41 | 603 | 501
V | 36 | 1167 | 661 | 592
D | 408 | 671 | 1287 | 76
A | 644 | 591 | 117 | 1140
TABLE: Showing QBER and Key Rate for BBM92 Protocol
BOB
ALICE
Background Coincidences=40
Average Sift Key Rate = Total CC in correct basis detectors = 4.5 kbps
QBER= CC in wrong detectors/total CC= 4%
Secure key rate ~ 1.7 kbps

## Slide 15
Atmospheric conditions, mean and variance from midnight to 6 AM (typical measurement time for our experiments)
Date | Extinction (Mm-1) | Scattering (Mm-1) | PM2.5 (µg/m3)
08/05/2021 | 76.41±7.78 | 62.73±5.82 | 2.87±0.26
10/05/2021 | 48.67±6.70 | 40.16±6.15 | 1.68±0.24
Sarika et. al., Journal of Optics (2022)

## Slide 16
Creating Polarization Entanglement with varying visibility

## Slide 17
Variation of S with QBER

## Slide 18
Non-zero secure key rate

## Slide 19: QKD Network: PRL CDOT QKD Integration

## Slide 20
Effect of turbulence and how to mitigate it for terrestrial and satellite communication
Simulating conditions for uplink and downlink to check the key rate for satellite based quantum communication
Development of Device Independent QKD protocols
Entanglement swapping and quantum teleportation in free space for 200 meters towards setting QC network
Using structured light such as - Vortex beam, Pencil beam, Gaussian Schell Model beam, Twisted Gaussian Schell Model beam - for robust and secure key distribution
Development of Photonic Quantum Computing since it is the best bet for quantum internet, World Wide Quantum Web (WWQW), the ultimate stage of quantum communication (China, Xanadu in Canada and Psi Quantum in USA, ORCA Computing in UK are making good progress)
Future plan of work under QST Program @ PRL

## Slide 21: Thank You
“The greater danger for most of us lies not in setting our aim too high and falling short; but in setting our aim too low, and achieving our mark.”
Michelangelo

## Slide 22
Entangled photon source
Pump
@405 nm
Jabir et al “Robust, high brightness, degenerate entangled photon source at room temperature”, Scientific Reports 7 (1), 1-8 (2017)
QuantESS payload for entanglement
and HOM interferometer study in
space
Prototype
+

## Slide 23
Neutralizing effect of phase-matching parameters on SPDC ring size
405.01 nm
Singh, S. et.al., Adv Quantum Technol. 2023, 6, 2200121.
Notes: Change

## Slide 24: Bell-CHSH Violation
Gives indication about quantum entanglement
are the four different polarizer angles
CHSH-Bell Parameter
Correlation Coefficient
For Entangled state having polarizer setting
Bell-CHSH Violation

## Slide 25
Entanglement Source
1 | 0 | 1 | 1 | 0 | 0
1 |  |  | 1 | 0 | 0
N |  |  | N | N | Y
1 |  |  | 1 | 0 | 
Alice
Bob
1 | 0 | 0 | 1 | 0 | 1
1 |  |  | 1 | 0 | 1
N |  |  | N | N | Y
1 |  |  | 1 | 0 | 
Basis Selection
Bit Values
Sifting
Error Checking
Key
110
110




BBM92 Protocol

## Slide 26
Experimental Implementation of BBM92 Protocol
Entangled Photon Source, Launching Optics
Collecting Optics, Alice Detection Setup and Time Tagger
Collecting Optics, Bob Detection Setup and Time Tagger
Quantum Channel
Quantum Channel
Classical Channel
ALICE
BOB

## Slide 27
Optical Setup for BBM92 Protocol
Launching Optics
Collecting Optics
Polarization State Analysis
PBS
HWP
SPCM
MMF
To BOB
From ALICE
SPCM
SMF
BOB
ALICE
PBS
BS
BS
PBS
HWP
Entangled Photon Source
Oscilloscope

## Slide 28
Entanglement distribution over 200 meters

## Slide 29
Correlation of polarization states between Alice and Bob
Coincidence window = 1 ns
H | V | D | A
94.2% | 93.66% | 83.33% | 87.53%
Bell’s Parameter
S=2.54 ± 0.06
Polarization Visibility
Entanglement Distribution over 200 meters

## Slide 30
Temporal Filtering
C.C. Window = 1ns
Delay from Alice’s H pol. state detector to Bob’s H pol. State detector = 648ns
Integration Time = 40ms
Delay x 10 ns
Counts

## Slide 31
Parameter Estimation for BBM92 Protocol
Channel Transmissivity =0.70 Overall Detector Efficiency=0.4
 | H | V | D | A
H | 1023 | 41 | 603 | 501
V | 36 | 1167 | 661 | 592
D | 408 | 671 | 1287 | 76
A | 644 | 591 | 117 | 1140
TABLE: Showing QBER and Key Rate for BBM92 Protocol
BOB
ALICE
Background Coincidences=40
Average Sift Key Rate = Total CC in correct basis detectors = 4.5 kbps
QBER= CC in wrong detectors/total CC= 4%
Secure key rate ~ 1.7 kbps

## Slide 32
Atmospheric conditions, mean and variance from midnight to 6 AM (typical measurement time for our experiments)
Date | Extinction (Mm-1) | Scattering (Mm-1) | PM2.5 (µg/m3)
08/05/2021 | 76.41±7.78 | 62.73±5.82 | 2.87±0.26
10/05/2021 | 48.67±6.70 | 40.16±6.15 | 1.68±0.24
Sarika et. al., Journal of Optics (2022)

## Slide 33: QKD Network: PRL CDOT QKD Integration

## Slide 34
Ministry of Communications
C-DOT & PRL demonstrate integration of indigenous Fiber based Quantum Key Distribution system with Free Space QKD system leading end to end quantum communication link in both Fiber and Free space as transport medium
Posted On: 05 MAR 2024 6:26PM by PIB Delhi
C-DOT & PRL Achieve Significant Milestone: In a first in the country, both the organizations demonstrate integration of CDOT’s indigenous Fiber based Quantum Key Distribution (QKD) system with Free Space QKD system from Physical Research Laboratory (PRL) leading to establishment of an end-to-end quantum
communication link involving both Fiber and Free space as transport medium.
The end-to-end quantum communication link with C-DOT’s Fiber-based QKD integrated with PRLs free space QKD was demonstrated to Prof. Ajay Sood, Principal Scientific Adviser to the Government of India and Dr Neeraj Mittal, Secretary Department of Telecommunications, Government of India during 2nd International Quantum Communication Conclave held at Vigyan Bhawan, New Delhi.
…………….
Press Release

## Slide 35
Effect of turbulence and how to mitigate it for terrestrial and satellite communication
Simulating conditions for uplink and downlink to check the key rate for satellite based quantum communication
Development of Device Independent QKD protocols
Entanglement swapping and quantum teleportation in free space for 200 meters towards setting QC network
Using structured light such as - Vortex beam, Pencil beam, Gaussian Schell Model beam, Twisted Gaussian Schell Model beam - for robust and secure key distribution
Development of Photonic Quantum Computing since it is the best bet for quantum internet, World Wide Quantum Web (WWQB), the ultimate stage of quantum communication (China, Xanadu in Canada and Psi Quantum in USA, ORCA Computing in UK are making good progress)
Future plan of work under QST Program @ PRL

## Slide 36: Thank You
“The greater danger for most of us lies not in setting our aim too high and falling short; but in setting our aim too low, and achieving our mark.”
Michelangelo